Menlo Park Fire Protection District

### Fire Prevention Bureau

170 Middlefield Road

Menlo Park, CA 94025

Phone: (650) 688-8425     Fax: (650) 473-9847

MENLO PARK FIRE PROTECTION DISTRICT

GUIDELINE FOR THE INSTALLATION OF TRAFFIC CALMING DEVICES

Section 503.4.1 Traffic Calming Devices

Scope.  When allowed by the fire code official, the installation of any traffic calming device shall be in accordance with Federal, State, and County guidelines and the requirements set forth in this Standard.

Emergency Response Issues:

- Concern over jarring of emergency rescue vehicles

- Approximate delay of between 3 and 5 seconds per hump for fire trucks and up to 10 seconds for ambulances with patients

Locations.  Traffic calming devices shall not be allowed on designated fire apparatus response routes, see attached map.  When approved by the fire code official, traffic calming devices shall be installed in accordance with the following Federal Highway Administration guidelines:

- Traffic calming devices may only be installed on residential streets.  They shall not be used on major roads, bus routes, or primary emergency response routes.

- Speed humps shall not be placed mid-block or at intersections.

- Traffic calming devices shall not be located on grades greater than 8 percent.

- The maximum height of a speed hump shall not exceed 3.5 inches.

- In accordance with San Mateo County Policy, speed humps shall not be placed on streets where posted speed limits are 30 miles per hour or more.

Installation of traffic calming devices.  When allowed by the fire code official, traffic calming devices such as roundabouts or other devices that are meant to disrupt the normal flow of traffic, such devices shall be installed in a manner that does not obstruct the required width of a fire lane as specified by Section 503.2.1 of the California Fire Code.

Installation of speed humps.  Speed humps may be installed in accordance with the Federal Highway Administration Manual on Uniform Traffic Control Devices or the attached San Mateo County Department of Public Works traffic humps drawing.